## Slide 1: StayAwake
Driver Drowsiness Detection system
Capstone Project Phase B
Supervisor: Aliza Attaly
Students:
Dvir Ben-Simon
Arik Zagdon
1

## Slide 2: Introduction
Describe the need for the system
2

## Slide 3
Drowsy driving responsible for about 100,000 crashes and 71,000 injuries every year
27% of the drivers admit that they are driving while being tired
3

## Slide 4: Statistics
Drowsy Drivers involved in fatal crashes
Fatalities caused by drowsy drivers
4

## Slide 5: What are the signs of drowsy driving?
Constant blinking
frequent yawning
Long blinking duration (snooze)
Having trouble keeping your head up
Weaving between lanes
5

## Slide 6: Development Process
6

## Slide 7
Project Start,
phase A
Design & Architecture
Development
Brainstorm,
Select project
Verification
Research
Investigate drowsiness detection projects
UML Diagrams, define which technologies to work with
Implement the
solution in python
7

## Slide 8: StayAwake System
Driver drowsiness detection
8

## Slide 9: System Hardware Components
Mini-PC
Camera
Monitor
9

## Slide 10: System Hardware Components
10
System Assembled

## Slide 11: System Software How does it work?
Face detection and point landmark extraction using Dlib library, giving us 68 landmark points of the face
11

## Slide 12: How does it work? System Software
Closed Eye detection
12
Average EAR from both eyes

## Slide 13: How does it work? System Software
Open Mouth Detection
13

## Slide 14: How does it work? System Software
Head Pose Detection
14

## Slide 15: StayAwake System
Driver fatigue analyzation
Hazard mode
Blinks per minute
Yawning
Snooze
Eye closed
Head fallen
15

## Slide 16: StayAwake System
16

## Slide 17
Blinks per minute
Driver fatigue analyzation
17
< 0.19
Count the number of detected blinks per minute, using the eye aspect ratio calculated in each frame. The EAR should be below 0.2 and blink duration between 50 ms to 150 ms
If the blinks per minute exceed 25 blinks, it add a fatigue sign to drowsy indicator variable

## Slide 18
Yawning
Driver fatigue analyzation
Detect yaw using mouth aspect ratio that calculated in each frame The MAR should be higher than 0.2
If yawning is occurred, It add to the drowsy indicator variable
18
0.2

## Slide 19
Snooze
Driver fatigue analyzation
19
< 0.19
0.15<duration<0.5
blink
Detect snooze using eye aspect ratio that calculated in each frame and blink duration. The EAR should be below 0.2 and blink duration between 150 ms to 500ms
If snooze is occurred, It add to the drowsy indicator variable

## Slide 20
Driver fatigue analyzation
Feature Score | Trigger
Risky blinks (B) | BPM > 25
Yawning (Y) | Yaw detected
Snooze (S) | 0.15s < Blink duration > 0.5s
This three features counted during five minutes time window, and when time windows is ended the system calculate driver drowsy indicator by the follow formula:
20
Every time window, if the drowsy indicator is exceed 10, the fatigue level is increased by one, and appropriate message is displayed and sounded to the driver
The system have 5 different fatigue level, and every fatigue level has a different message.

## Slide 21
Eye closed
Hazard Mode
Detect if the eye closed for more than 500 milisecond
Sound noisy alarm in order to wake the driver up
21
Blink_duration>0.5
< 0.19

## Slide 22
Falling head
Hazard Mode
Detect if the head angle dedicated as fallen
Sound noisy alarm in order to wake the driver up
22

## Slide 23: Project Diagram
23

## Slide 24: Use Case
24
Display Message on monitor

## Slide 25: Package Diagram
25

## Slide 26: Deployment
26

## Slide 27: Activity Diagram
27

## Slide 28: Project Evaluation
28

## Slide 29
29
We calculated the confusion matrix with the parameters describe below, in order to measure the effectiveness of the system.
True Positive - The driver doing drowsy feature and the system recognized it
True Negative - The driver didn’t do drowsy feature and the system didn’t recognized it
False Positive - The driver didn’t do drowsy feature but the system recognized it as a drowsy feature.
False Negative - The driver doing drowsy feature and the system didn’t recognized it as a drowsy feature
In our project we used accuracy evaluation

## Slide 30: Experiment & Result
30

## Slide 31: Experiment 1: EAR Thresholding
31

## Slide 32: Experiment 2: MAR Thresholding
32

## Slide 33: Results
33
Drowsiness detection
We test all of the features of our system accuracy.
We did 100 times of evry feature.

## Slide 34: Results
34
Sleep detection
The total accuracy of the system is calculated as the average of all features accuracy:

## Slide 35
Demonstration
35

## Slide 36: Challenges & Conclusions
36

## Slide 37
Challenges
We got poor performance when debugging the first version of our software on the raspberry pi, because of high image processing stages.
When the driver blinked the system counted more than one blink, because of the system take account each frame below the threshold as a blink.
When the system sound an alarm or notifications the all system freezes until the sound is over, this issue stop the recognition process.
37

## Slide 38
Conclusions
The system can avoid car accident causing of drowsy driver
Put more effort into the face recognition field, to increase the system’s performance and accuracy
Experiment the hardware specification in advance, especially in image processing systems
38

## Slide 39: Thank You
39